DAEDALUS - Descent And Exploration
in Deep Autonomy of Lava
Underground Structures

---
Exploring and characterising the entrance and initial part of Lunar lava tubes
- A compact, tightly integrated spherical robotic device
- A sphere is ideally suited to protect sensors and scientific equipment in rough, uneven environments.

---
Exploring and characterising the entrance and initial part of Lunar lava tubes
- The tether for lowering the sphere will be used for data communication and powering the equipment during the descending phase
- Furthermore, the connector tether-sphere will host a WIFI access point, such that data of the conduit can be transferred to the surface relay station.

---
Camera System
- panoramic lens
- dual-lens system
  for stereo
  (3D data)

---
Laser Scanner
- LiDAR systems work at any illumination conditions
- Direct 3D data, computationally easy to handle
- SLAM for creating 3D maps throughout the whole mission

---
Rolling using
- with spikes and pods, the sphere robot is able to overcome obstacles of about half of its own diameter.

---
Communication
- The communication with the surface will be tethered or, eventually, Wi-FI based
- The deployment rover will be enabled to communicate with the remote control room

---
Crane for lowering the sphere
- Rim stability is to be accurately studied
- double fixing points may prevent possible uprooting of the anchors

---
Current Workplan
WP	Name	Lead
1	Coordination (gitlab, owncloud, LaTeX, … )
2	Robotic Sphere for Descent	JMUW
2.1	Overall Sphere Design
2.2	Locomotion
2.3	The Sensing Subsystem (Camera, LiDARs,...)
3	Geology and Spectral Requirements	UNIPD
3.1	Landing Site Characterization
3.2	Spectral Capabilities Definition/Response to Scientific Requests
3.3	Instrument Integration in the Sphere

---
Current Workplan, cont.
WP	Name	Lead
4	Optics	INAF
4.1	Optical Performance in Lunar Environment
4.2	Dust Removal
4.3	Structure-from-Motion and LiDAR-SLAM
4.4	Instrument Integration in the Robot
5	Testing/Simulation	VIGEA
- The work package structure will superimpose a structure to the final CDF document
- The work packages will be accompanied by real-world experiments

---
Contact
Andreas Nüchter
University of Würzburg
Robotics and Telematics
Am Hubland
97074 Würzburg, Germany
andreas@nuechti.de or
andreas.nuechter@uni-wuerzburg.de
http://www.nuechti.de
https://www.youtube.com/channel/UC7HAqZXI-jvMmBwoi4vDUew